## Slide 1: CNES Real-time Analysis center Status
    Real Time analysis center since 2011
    Supported messages (5 sec sampling)
      GPS orbits and clocks
        Orbits retrieved from various sources and improved using real-time measurements
        Orbits quality around 3 cm
        Clocks standard deviation less than 0.1 ns
      Glonass orbits and clocks
      GPS and Glonass code biases (Bern DCBs)
      GPS Phase biases for ambiguity resolution on isolated receivers
    Ongoing work
      Switch to MSM messages thanks to the MGEX network
      L5 phase bias computation for 3-freq ambiguity resolution on blocks IIF
      Galileo clocks computation (ultra-rapid orbits provided by DLR for preliminary tests)

## Slide 2: Ambiguity fixing group
    Purpose of the group
      To participate in the RTCM standardization process for SSR phase biases messages from the IGS point of view
      Geo++ is in charge of this standardization
      Group is composed of :
        BKG, CNES, CTUP, DLR, ESOC, Geo++, GFZ, NrCan
      After some corrections and changes, Geo++ issued a document in version 6 (final) in May 2014
    Main ingredients of phase biases messages
      One phase bias per observable (same convention as SSR code bias)
      Satellite yaw information (for combinations of solutions)
      Continuity indicator (to reset ambiguity vector at user level)
      Other indicators (WL/NL integer ambiguity, dispersive signal)
    CNES computes and generates phase biases for GPS (streams CLK9x)
      IGS mail #6916
      Allows ambiguity resolution on GPS
      Ongoing encoding/decoding interoperability tests with Geo++